## Slide 1
AI Agents for Biomedical Engineering
From EMG Signals to Intelligent Prosthetic Hand Control
Hands-on Engineering Workshop
1

## Slide 2
The Engineering Problem
How can a machine understand what a human muscle intends to do?
EMG signal → muscle activity → human intention → prosthetic action
2

## Slide 3
What Is EMG?
Electromyography (EMG) captures electrical activity produced by muscles.
Electrodes → electrical signal → sampled waveform
Today we will use a simulated EMG signal so the complete agent pipeline can run locally.
3

## Slide 4
From Raw Signal to Information
Raw EMG is noisy and difficult to interpret directly.
Signal processing gives us measurable features:
• RMS — signal power / activity level
• MAV — average absolute amplitude
• Activation window — when the muscle is active
4

## Slide 5
Hands-on Lab 1 — Analyze EMG
Run:
python 03_emg_tool.py
Observe:
• Raw EMG waveform
• Windowed RMS
• Activation start/end
• RMS and MAV
Question: What changes when the muscle becomes active?
5

## Slide 6
The Missing Piece
Measuring muscle activity is not enough.
The system needs to convert measurements into an intention:
REST → REST
OPEN → OPEN
CLOSE → CLOSE
That is our gesture-classification layer.
6

## Slide 7
Hands-on Lab 2 — Gesture Classification
Run:
python 05_emg_gesture_tool.py
The tool generates three reproducible EMG patterns and classifies them using RMS.
REST → REST
OPEN → OPEN
CLOSE → CLOSE
7

## Slide 8
From Software to Actuator
Now we need something that responds to the decision.
Run:
python 04_prosthetic_hand.py
Try:
OPEN
CLOSE
REST
This is our virtual prosthetic hand.
8

## Slide 9
What Is an AI Agent?
An LLM alone mainly generates responses.
An AI agent can:
• Observe information
• Reason about it
• Choose what to do
• Use tools
• Take an action
• Continue the loop
AI Agent = Brain + Tools + Decision + Action
9

## Slide 10
Anatomy of Our Biomedical Agent
Brain: Gemma 4 running locally with Ollama
Biomedical tools:
• EMG analysis
• Gesture classification
• Prosthetic-hand control
Environment:
Virtual prosthetic hand
Everything runs locally on the student's machine.
10

## Slide 11
The Agentic Loop
OBSERVE
↓
ANALYZE
↓
DECIDE
↓
ACT
↓
OBSERVE AGAIN
The important difference: the AI is part of a system that can make a decision and trigger an action.
11

## Slide 12
Hands-on Lab 3 — First Integration
Run:
python 06_biomedical_ai_agent.py
Watch the complete flow:
EMG → analysis → gesture → AI decision → hand action
Look for the final hand state.
12

## Slide 13
Hands-on Lab 4 — Give the System a Brain
Run:
python 07_true_biomedical_agent.py
The system sends measured biomedical results to Gemma and asks the AI agent to decide:
REST / OPEN / CLOSE
Then the selected action is executed by the simulator.
13

## Slide 14
Complete System
HUMAN
↓
MUSCLE ACTIVITY
↓
EMG SIGNAL
↓
SIGNAL PROCESSING
↓
GESTURE / INTENTION
↓
AI AGENT
↓
DECISION
↓
PROSTHETIC HAND
A complete perception → decision → action pipeline.
14

## Slide 15
Why Use an Agent?
Traditional fixed pipeline:
Signal → fixed rule → action
Agentic pipeline:
Observe → reason → choose → use tools → act
The agent becomes useful when the system has multiple tools, changing context, or multiple possible actions.
15

## Slide 16
Student Challenge + Safety Discussion
Challenge:
• Add GRIP as a new gesture
• Add a new actuator behavior
• Design a real EMG sensor architecture
Discussion:
Would you let an AI agent control a real prosthetic device?
Consider human oversight, fail-safe behavior, false positives, latency, validation and regulation.
The future isn't just AI that answers. It's AI that can perceive, reason, use tools and act — safely.
16